## Slide 1: Self-Balancing Cube
Iustinian Serban Bogdan

## Slide 2: Contents
Project Overview
01
Methodology
02
System Architecture
03
Control System Design
04
Testing
05
Next Steps
06
Bibliography
07

## Slide 3: Project Overview
Design and implementation of a self-balancing cube (Cubli) that uses reaction wheels and a gyroscope to maintain balance on one of its edges or corners.
Objectives:
  Design and assemble a medium-scale Cubli. ✅
  Implement a control system to balance the Cubli on its edge using feedback from sensors. ⁉️
  Tune and optimize the PID controllers to ensure stability and fast recovery from perturbations. ✅
  Demonstrate the cube’s ability to balance autonomously after disturbances. ❌

## Slide 4: Methodology – Reaction Wheels
A reaction wheel is a spinning mass mounted inside the cube. When the motor changes the wheel’s rotational speed, the cube experiences an equal and opposite torque (due to the conservation of angular momentum).
Accelerating a reaction wheel clockwise applies a counterclockwise torque to the cube.
Decelerating or braking the wheel applies torque in the opposite direction.

## Slide 5: Methodology – PID Controller
A PID controller is a widely used feedback control mechanism that calculates an error value between a desired setpoint and a measured process variable and then applies a corrective action to minimize that error over time.
Proportional (P): Corrects the error in proportion to its current size.
Integral (I): Corrects accumulated past errors by integrating over time.
Derivative (D): Predicts future errors by calculating the rate of change.

## Slide 6: Methodology – PID Controller
A PID controller is a widely used feedback control mechanism that calculates an error value between a desired setpoint and a measured process variable and then applies a corrective action to minimize that error over time.
Proportional (P): Corrects the error in proportion to its current size. ✅
Integral (I): Corrects accumulated past errors by integrating over time. ✅
Derivative (D): Predicts future errors by calculating the rate of change. ❌

## Slide 7: System Architecture – Electronic Components
ESP32-DevKitC 38 Pins
DF-SEN0142 IMU 6DOF
Expansion Board for ESP32
DF-DFR1015 Buck Converter
1800mAh 14.8V LiPo Battery
Nidec 24H Motors

## Slide 8: System Architecture – Mechanical
Custom Model in Fusion 360
3D Printed Parts in PLA
COTS Components
Plate with Mounting Holes
Motor Bracket
Electronics Support
Corner Piece

## Slide 9: System Architecture – Mechanical
Reaction Wheel
Aluminum Mounting Hub
Brass Inserts
M3/M4 Screws and Nuts

## Slide 10: System Architecture – Assembly
Motor Assembly
Electronics Assembly
Main Assembly

## Slide 11: System Architecture – Connection Diagrams
Power Lines
Data Lines

## Slide 12: Control System Design – Motor Data Acquisition
Data Lines

## Slide 13: Control System Design – Transfer Functions
MotorID | ID1 (Marcel) | ID2 (Daniel) | ID3 (Ghica)
TF |  |  | 
Discrete TF |  |  | 
NMSE | 2.3033 | 1.8369 | 2.0452
MotorID | ID1 (Marcel) | ID2 (Daniel) | ID3 (Ghica)
NMSE | 2.3033 | 1.8369 | 2.0452
Identification with the MATLAB’s build-in ARX function
Metric for TF accuracy:
(Normalized Mean Square Error)

## Slide 14: Control System Design – PI Tuning
MotorID | ID1 (Marcel) | ID2 (Daniel) | ID3 (Ghica)
Discrete Controller |  |  | 
Settling Time [s] | 0.651 | 0.648 | 0.651
Overshoot [%] | 13.1 | 13.1 | 13.1
MotorID | ID1 (Marcel) | ID2 (Daniel) | ID3 (Ghica)
 | 0.651 | 0.648 | 0.651
 | 13.1 | 13.1 | 13.1
Controller tuning using MATLAB’s build-in pidtune function:
[c_tuned, info] = pidtune(Hf_discret, 'PI', 13.33)
,
Imposed performances
Settling time
Overshoot

## Slide 15: Testing

## Slide 16: Next Steps
Develop the Cubli as part of the Bachelor’s thesis
Test and integrate the IMU into the control system to enable full closed-loop balancing control
Refine the 3D mechanical design to achieve a more compact structure and reduce unnecessary space
Replace 3D-printed components with precision-machined aluminum parts
Explore a more robust control strategy

## Slide 17: Bibliography
ETH Zürich, Cubli: A Cube That Can Jump Up, Balance, and Walk Across Your Desk. [Online Video]. Available: https://www.youtube.com/watch?v=n_6p-1J551Y
Åström, K. J., & Hägglund, T., PID Controllers: Theory, Design, and Tuning. Instrument Society of America, 1995.
MathWorks, pidtune (PID Tuning) - MATLAB Documentation. [Online]. Available: https://www.mathworks.com/help/control/ref/pidtune.html
Texas Instruments, Brushless DC Motor Fundamentals. [White Paper]. Available: https://www.ti.com/lit/an/slyp173/slyp173.pdf
DFRobot, DF-SEN0142 MPU6050 6DOF IMU Datasheet. [Online]. Available: https://wiki.dfrobot.com
DFRobot, DFR1015 Buck Converter Module. [Product Page]. Available: https://wiki.dfrobot.com/DFR1015
Espressif Systems, ESP32 Technical Reference Manual. [Online PDF]. Available: https://www.espressif.com/en/products/socs/esp32/resources
Nidec Corporation, Nidec 24H Series Brushless DC Motor Specifications. [Datasheet]. Available: https://www.nidec.com